## Slide 1: A S T A
- Automatically Sleep Terminate Assistant -
Digital Control Systems Technology
Faculty of Technology
University of Sri Jayewardenepura
2023 . 06 .15

## Slide 2: PROJECT OVERVIEW 01 BLOCK DESIGN CONSTRUCTION & TESTING COMPONENTS TABLE OF CONTENTS
03
05
02
04
CIRCUIT DIAGRAM

## Slide 3
The goal of this project is to develop a system that can accurately detect sleepy driving and make alarms accordingly, which aims to prevent the drivers from drowsy driving and create a safer driving environment.
The project was accomplished by a Webcam that constantly takes image of driver, a beagle board that implement image processing algorithm of sleepy detection, and a feedback circuit that could generate alarm and a power supply system.
PROJECT OVERVIEW

## Slide 4: BLOCK DIAGRAM

## Slide 5: CIRCUIT DIAGRAM

## Slide 6: WEB CAMERA AEDUINO UNO Hardware COMPONENTS ( 16 x 2 ) LCD Display

## Slide 7: Push Button Switch Hardware COMPONENTS Buzzer Wires Battery & Power Supply HC-03 Bluetooth Model

## Slide 8: COMPONENTS
Hardware manipulation
Build front-end interface
Python
Back-end works
Image processing
Image processing library

## Slide 9: CONSTRUCTION & TESTING
import cv2
import serial
import time
# Config the arduino
# ArduinoSerial = serial.Serial('COM8', 9600, timeout=1)
ArduinoSerial=serial.Serial('COM4', 9600, timeout=1) #Start communications with the bluetooth unit
face_cascade = cv2.CascadeClassifier('open/cascadeFace.xml')
eye_cascade = cv2.CascadeClassifier('open/eyeGlass.xml')
cap = cv2.VideoCapture(0)
while cap.isOpened():
time.sleep(0.5)
key = 0
ret, frame = cap.read()
gray = cv2.cvtColor(frame, cv2.COLOR_BGR2GRAY)
faces = face_cascade.detectMultiScale(
frame,
scaleFactor = 1.1,
minNeighbors = 6,
minSize = (350, 350)
)
for x, y, w, h in faces:
cv2.rectangle(frame, (x, y), (x + w, y + h), (0, 0, 255), 3)
face = frame[y:y + h, x:x + w]
eyes = eye_cascade.detectMultiScale(
face,
scaleFactor = 1.1,
minNeighbors = 6
)
for x2, y2, w2, h2 in eyes:
cv2.rectangle(face, (x2, y2), (x2 + w2, y2 + h2), (0, 255, 0), 3)
key = 1
cv2.imshow('img', frame)
if cv2.waitKey(10) & 0xFF == ord('q'):
break
print(key)
cnvKey = str(key)
ArduinoSerial.write(cnvKey.encode('utf-8'))
cap.release()
cv2.destroyAllWindows()
Python

## Slide 10: CONSTRUCTION & TESTING
#include "SoftwareSerial.h"
#include <LiquidCrystal.h>
const int rs = 7, en = 9, d4 = 8, d5 = 6, d6 = 5, d7 = 4;
LiquidCrystal lcd(rs, en, d4, d5, d6, d7);
SoftwareSerial serial_connection(2, 3);//Create a serial connection with TX and RX on these pins
int led_pin = 11;
#define switch A0
char inChar=-1;//Initialie the first character as nothing
int count =0;
void setup()
{
lcd.begin(16, 2);
pinMode(11, OUTPUT);
Serial.begin(9600);//Initialize communications to the serial monitor in the Arduino IDE
Serial.println("Started");//Tell the serial monitor that the sketch has started.
lcd.setCursor(1 , 0 );
lcd.print("Project ASTA");
delay(1000);
}
void loop()
{
byte byte_count=serial_connection.available();//This gets the number of bytes that were sent by the python script
if(byte_count)//If there are any bytes then deal with them
{
Serial.println("Incoming Data");//Signal to the monitor that something is happening
inChar=serial_connection.read();//Read one byte
while(inChar == '1'){
digitalWrite(led_pin,LOW);
clr(2);
lcd.setCursor(1 , 1 );
lcd.print("Drive Safe");
// delay(1000);
inChar=serial_connection.read();//Read one byte
while(inChar != '1' && count < 10){
inChar=serial_connection.read();//Read one byte
delay(200);
count++;
Serial.println(count);
}
count = 0;
}
Serial.println(inChar);//Print to the monitor what was detected
}
while (1){
digitalWrite(led_pin, HIGH);
clr(2);
lcd.setCursor(1 , 1 );
lcd.print("SLEEP WARNING!");
int val = digitalRead(switch);
delay(20);
if(val == HIGH)
break;
}
}
void clr(int x) {
lcd.setCursor(7, x-1);
lcd.setCursor(0,x-1);
lcd.print(" ");
}

## Slide 11: CONSTRUCTION & TESTING

## Slide 12: BUDGET
Name | Price (Rs:)
Arduino UNO | 2,950.00
Bluetooth Module ( HC-05 ) | 950.00
( 16 x 2 ) Blue Backlight LCD Display | 700.00
Project Board ( Breadboard Solderless ) | 360.00
Jumper wire ( Male-to-Male ) | 240.00
Battery ( 9V ) | 180.00
Glue Sticks ( Small ) | 70.00
Mini Buzzer ( 5V ) | 60.00
Potentiometer (10K ) | 30.00
Push on Switch ( 4-pin ) | 20.00
NPN Transistor (D400 ) | 20.00
LED ( 5mm White ) | 10.00
Resistors [ 100k ( Kilo ohm ) ] | 2.00
Total | 5592.00
360.00

## Slide 13: RESOURCES
OpenCV – Documentation
  https://docs.opencv.org/4.x/
GitHub – Repository
  https://github.com/GeekyShiva/OpenCV-miniProject-FaceDetection
Arduino – Documentation
  https://www.arduino.cc/en/Guide
Sackoverflow - Forums
  https://stackoverflow.com

## Slide 14: PROJECT PERFORMANCE 10% 40% 50% SPEED EFFICIENCY PREDICTION
Mercury is the closest planet to the Sun and the smallest of them all
Follow the link in the graph to modify its data and then paste the new one here. For more info, click here
Venus has a beautiful name and is the second planet from the Sun
Mars is full of iron oxide dust, which gives the planet its reddish cast

## Slide 15: The TEAM
Mudara Manaruchira - ICT/20/886
Nusrath Suhaila-ICT/20/942
Yasasi Ravihansi - ICT/20/812
Shavindu T. Sampath - ICT/20/923
Asitha Lakmal - ICT/20/935
Chathuka Bimsara-ICT20/815
Fathima Faazath - ICT/20/839
Fathima Rustha - Ict/20/920

## Slide 16: THANK YOU